## Slide 1: Literature Review
SAYAK KARMAKAR
ROLL NO: 22CE92R05

## Slide 2
Sara Barbieri et al., 2023
Numerical procedure for simulating borehole heat exchangers operation and interpreting thermal response test (TRT) through MODFLOW-USG code.
Novelty: The introduction into the CLN package of new characteristic elements of a Borewell Heat Exchanger (Such as the thickness and the thermal conductivity of the U-pipe and the internal convective heat transfer coefficient).
The DRT (Drain Return Flow) package available in MODFLOW-USG-Transport was modified to accommodate condition of constant heat rate injection.
Important points: A total of 16 different models are implemented combining 4 minimum cell size values (0.5-50 cm) and 4 Darcy velocity(10-5,10-6,10-7, 0 m/s). Quadtree refinement around the BHE was used.

## Slide 3
Simulation of TRT is done for longer period of time (60 days)
The solver used for the numerical simulations is the Sparse Matrix Solver (SMS), which includes a Total Variation Diminishing (TVD) scheme to control numerical dispersion in the advection term.
Validation: Evaluation of the model validation was through the aquifer temperature values in correspondence of 11 monitoring wells. RMSE error was calculated at different time steps.
Evaluation of the model was carried out through the analytical models ILS/MLS of the aquifer temperature values downstream of the BHE.
Observation: Implementation of coarse grids lead to an underestimation of the heat carrier fluid mean temperature. Maximum error in heat rate estimation using the numerical model was 3.8%.

## Slide 4
Vivek Bedekar et al.,2019
Axisymmetric modelling using MODFLOW-USG (with unstructured grids) for : (i) a pumping well with delayed yield effects, (ii) a vadose zone flow model simulating an infiltration basin and (iii) a density-dependent saltwater intrusion problem for a circular island.
Novelty: A preprocessing program was developed to write the DISU file (required to define coaxial cylindrical cells) of MODFLOW-USG by reading user-defined NLAY, NCOL, and horizontal and vertical cell spacing.
Heterogeneity may be introduced without recalculating any surrogate parameters like previous methodologies.
Pumping well: Dimensionless drawdown vs time curve of Numerical Model was compared with analytical solution provided by Neuman , 1974 (was solved using the software AQTESOLV) and a full 3D model in MODFLOW-USG. The well was a partially penetrating well in unconfined aquifer in homogenous and isotropic media.

## Slide 5
Vadose zone flow: sandy aquifer with confining unit at the middle. Comparison was done to evaluate the infiltration capacity of circular infiltration basin using Axisymmetric and 3D models of MODFOLW-USG.
Saltwater intrusion: circular island surrounded by seawater on all sides with recharge applied on top. Two axisymmetric models results obtained using ‘BCT package of MODFLOW-USG’ and ‘axisymmetric SEAWAT model’ were compared with analytical solution provided by Fetter (1972), 3D MODFLOW-USG and 3D SEAWAT model. Steady-state saltwater-freshwater interface was compared for the models.
Comments: Transport equation for MODFLOW-USG and SEAWAT models using upstream-weighted finite difference scheme gives more numerical dispersion than TVD scheme.
Run time for axisymmetric model is in order of minutes, but, for 3D it is in order of days.

## Slide 6
Christian D. Langevin et al., 2020
Density-dependent groundwater flow and transport modelling using hydraulic head formulation and result compared with previous freshwater head formulations like SEAWAT, laboratory experiments etc.
Characteristics & Novelty: Darcy’s Law can be written as the sum of the well-known, constant-density, hydraulic-head term.
Control volume finite difference method is used having some correction terms in the system of equations of constant-density groundwater modelling to include variable density effect.
Approach is same as MOCDENS3D, but MOCDENS3D is based on freshwater head formulation. Head based variable density code, such as SEAWAT is also based on freshwater head formulation.
Freshwater-head formulation typically requires repeated conversion between freshwater head and hydraulic head within the modelling code to determine whether cells are confined, unconfined, or dry. So, freshwater approach makes Jacobian derivative terms more complex and problem occurs in terms of convergence to the solutions.
The discussions is in terms of MODFLOW-6 and MODFLOW-USG, but can be implemented for Hydrus, MIKE SHE, MODFLOW/MT3DMS .

## Slide 7
Code is validated with four different Example :
Example 1- Henry Problem: Two types of simulation were done: (i) Original Henry problem and (ii)low inflow henry problem. Low inflow ensures less ‘advective dominant’ and more ‘density driven’ flow. Both simulations were performed for two cases: specified BC ( boundary is considered as fixed conc. as seawater) and mixed BC (inflow boundary has same conc. as seawater but outflow boundary conc is calculated based on the conc. of outmost cell).
Example 2- Rise and fall of the seawater level: Hydraulic head formulation with fluctuating seawater level as boundary condition to simulate rise and fall of water table. Total simulation period was 1.25 days (for 1st 0.25 days, seawater level was considered as constant!!). Relative salinity contour lines were plotted for different seawater level at different times.
Example 3- Saltwater Intrusion Laboratory Experiment: Rectangular flow tank with dimensions of 53 cm (length) by 30.5 cm (height) by 2.7 cm (width). Three steady states were achieved using three different combinations of inflow and outflow head boundary. Relative salinity contours of MODFLOW-6 were compared with experimental data as well as with SEAWAT. But MODFLOW-6 dispersion (based on implicit 2nd order TVD scheme) shows more numerical dispersion than SEAWAT (based on explicit 3rd order TVD scheme).

## Slide 8
Example 4- Natural Convection Elder Problem: A common test for coupled variable-density flow and transport models. Two different simulations were performed:
for Rayleigh number=400; (higher Ra show the performance of hydraulic head formulation for larger density contrast flow).
For Ra=60; (lower Ra value is good for benchmarking, because for that only one solution exists).
Model was divided into 52 layers for 180 m thickness. For top and bottom layers, very low hydraulic conductivity were assumed ) to eliminate advective flow through these cells (why? These are unsaturated and confining zones?!).
Simulations were shown for 6, 20, 60, and 200 years and compared with SEAWAT, pseudo spectral results and FEFLOW results reported by van Reeuwijk et al. (2009).

## Slide 9
Christopher Muffels et al., 2022
Simulating groundwater interaction with a complex surface water network comprised of creeks, ponds, wetlands, springs using connected linear networks (CLN).
CLN is required because, SFR, LAK, CHD, RIV, DRN, WEL these packages from USG-TRANSPORT are purpose built and do not always interact with each other.
For connectivity of nodes IA/JA array specifications were used.
Seepage face properties like conduit radius, bed conductivity, length and thickness in original SFR, LAK & DRT packages were modified to apply in CLN package.
In CLN package, seepage faces were considered as circular, not rectangular.

## Slide 10
Advantages: CLN can consider two way flow simulations (E.g. Water discharges to wetland can further recharge GW system) unlike other packages.
Unlike LAK package, we do not need to inactive pond water cell. So, precise bathymetry and discretization are not required near to the pond.
Disadvantages: Some error may get introduced in the storage term in large water body where radius of CLN cells are small (i.e., flat bottom of the large surface water features).
Because of the circular seepage face of CLN cell, non-linearity is introduced in conductance formulations. So, CLN package takes more time for simulations.

## Slide 11
Matteo Antelmi et al., 2021
Simulation of thermal perturbation in groundwater caused by Borehole Heat Exchangers using an adapted CLN package of MODFLOW-USG.
Novelty: CLN package in MODFLOW-USG works on unstructured grids. So, coarser grids were applied here than previous works based on finite difference codes.
Model domain was 100m×50m ×160 m. Boundary conditions were constant head and temperature at left side and constant head at right side.
For CLN, BCs were prescribed inflow temperature and inlet flow rate (Neumann condition) and specific flow for outlet CLN node.
Three different models with 3 different grid sizes (6, 20, 50 cm) were developed in MODFLOW-USG one set with Quadtree refinement and other one without Quadtree refinement and coupled with CLN model of BHE.
Same models were run for 3 Darcy velocities 10-4,10-5 and 10-6 m/s to see how the heat transfer varies with change in the advection term.
These models were validated with a previous work in MT3DMS without CLN package. There minimum cell size was 0.37 cm. But, that convergence of that model was very tedious. But, in MODFLOW-USG, present authors did not require to find right set of solver parameters.

## Slide 12
Quadtree refinement is applied only cells near to the BHE’s (only where it is needed).
Finally, authors used those models to use CLN and quadtree refinement, to simulate 7 BHEs (oriented in a straight line in the way to GW flow) at the same time to evaluate overlapping effects of BHEs.
Results and Discussions:
Temperatures were measured at different points d/s of BHEs for 4 different periods of a year.
At outlet pipe, max temp difference to previous model was 0.6 ͦ C and for 5 m downstream of BHE it was 0.25 ◦C.
Limitations: CLN approach does not consider the convective heat transfer coefficient. Though, authors claimed, it does not affect much in results.
There was no experimental validation of this CLN based model in MODFLOW-USG. Even previous MT3DMS model was validated using a analytical result.

## Slide 13
NEVEN KRESIC et al. 2017
Numerical groundwater modelling in karst aquifer by coupling MODFLOW-USG with CLN package to introduce two Karst Conduits in model domain.
Novelty: Use of unstructured grids and FV approach of MODFLOW-USG
Most of the Previous works on Karst aquifers were based on time series analysis. So, availability of long time data for recharge and discharge was a problem.
Classic MODFLOW program can not simulate for high discrete medium, Darcy law is inadequate to simulate turbulent flow and model becomes instable while simulate large vertical displacement by faults and fractures.
Previously used EPM approach which works on averaging the hydraulic properties by incorporating surrogate parameters and can not simulate for real physical processes in highly heterogenous karst aquifers.
This current model solves four equations i.e. Hagen– Poiseuille equation for laminar flow Darcy– Weisbach equation, Hazen–Williams equation and Manning’s equation for turbulent flows which overcomes the limitations of classical MODFLOW codes.

## Slide 14
Methods and Discussions:
Two hypothetical karst conduits were formed using CLN at different elevations, each connecting a sinking stream and a karst spring. One string was permanent and another one was intermittent.
Model was divided into 12 layers each of 10m thick.
Model simulates for three time periods:
(i) one year long simulation and without recharge from the land surface.
(ii) simulation for two days of an areal recharge event from rainfall (0.15 cm/day) .
(iii) 30 days long simulation after the recharge event.
Results:
It shows a potentiometric surface map for different layers with wet and dry cells after time period (i),(ii) and (iii).
Simulates flow rates at two springs (permanent and intermittent) over time.
An additional conduit was introduced in layer 10 connected to north conduit and effect of that was shown in terms of equipotential lines.
Simulates fate and transport of contaminants from a constant rate source both for saturated and unsaturated zones.

## Slide 15
Neven Kresic et al., 2020
Dual porosity flow and transport formulation of non-aqueous phase liquid in coastal karst aquifer using MODFLOW-USG and CLN for coupling an aquifer matrix with karst conduit.
GWF modelling in karst has the following categories: Time-series models, EPM approach, Hydraulic models of pipe and/or reservoir networks, Coupled continuum conduit flow (CCCF) models. But, those have some drawbacks in formulation.
This work demonstrates the complex interactions between submerged karst conduits and the surrounding rock matrix in coastal areas.
The model has 100 columns, 50 rows and 12 layers.
Model bottom elevation is -52.5 m. Aquifer was considered as homogenous and isotropic.
Karst conduit has 2 ft radius, placed at -25 m elevation (i.e. 7th layer of the model). The conduit was discretized automatically by Groundwater Vistas from a 3D GIS shapefile.

## Slide 16
Results and Discussions:
The variable density steady-state simulations were performed for different conditions which includes:
Comparison of relative positions of freshwater-saltwater interface for steady-state model with conduit and without conduit both in map view of karst layer and cross-sectional view.
Comparison of the results of the steady-state model and the transient model for the end of 1 day of the rainfall in map and cross sectional view.
Comparison of seawater - saltwater interface for a transient model after a 5-day rainfall event with the scenario after 100 days of the rainfall event.
Pictorial representation of GW velocity vectors in the domain after 1 day and 5 days of rainfall event.
Relative salinity graph of 4 observation points over the simulation period. OP-1 was on the conduit, but far away from the shoreline. OP-3 was on the conduit, but after the shoreline. OP-2 was in between OP-1 and OP-3. OP-4 was a point in the aquifer matrix.